## Slide 1
Overview
Main Loop
  velocity command
  get base state & joint state
  calculate kinematics
  MPC
    decide stance / swing
    calculate contact forces with MPC
    calculate joint torques

## Slide 2
Velocity Command & Get States
acquire_actor_root_state
  position, rotation, linear velocity, angular velocity
acquire_dof_state
  position, velocity

## Slide 3
Compute Kinematics
Forward Kinematics
  input : joint position, base position
  output : feet position, jacobian

## Slide 4
Compute Dynamics
Update gait schedular
  Decide which leg is the stance (ground contact for power)
  Decide which leg is the swing (in the air, moving to the next landing point)
Prepare for MPC
  Enter the current robot states into the MPC internal state (x).
    base_pos, base_quat
    lin_vel, ang_vel
    q, q_dot
Run QP solver
  Calculate foot forces by solving a Quadratic Program (QP) at regular intervals
  Whether the leg can exert force or not is configured as a constraint through the gait table.

## Slide 5
Compute Dynamics : gait schedular
swing_states = gait.get_swing_state()
  Decide each leg is in swing or stance return.
  If in swing, calculate torque using the force output by the PD controller, if in stance, use the MPC.
gait_table = gait.get_gait_table()
  When the MPC predicts for a certain horizon ahead, it returns whether the leg is in stance or swing at each point in time.

## Slide 6
Compute Dynamics : MPC
predictive_controller.update_mpc()
  generate reference trajectory
  generate dynamics model
  discretize dynamics model
  generate QP constraints
generate dynamics model
  A: linear dynamics between robot base states (roll/pitch/yaw, pos, vel).
  B: Reflects how the foot force (u) accelerates/rotates the robot base.

## Slide 7
Compute Dynamics : MPC
QP constraints
  friction cone constraints
  gait constraints
    When in the swing position, the strength of the foot should be zero.
    When in the stance position, the foot force should be placed within the friction cone.
x_k : robot state
x_k_ref : desired state
Q : error weight
R : foot force weight
H, q : summary of the error, and u size as the second/first term.
=> 로봇이 레퍼런스와 멀어질수록 비용이 커짐, 발힘이 과도해도 비용이 커짐.

## Slide 8
Compute Dynamics : MPC

## Slide 9
Calculate joint torques
set_foot_placement
  Calculate the final position of the foot at the end of the swing.
compute_traj_swingfoot
  Create foot trajectory with cubic hermite interpolation (x, x_dot).
pos_targets_swingfeet
  Generate joint torque with PD controller when swing state.
  Generate joint torque with MPC when stance state

## Slide 10
Overview
Main Loop
  velocity command
  get base state & joint state
  calculate kinematics
  MPC
    decide stance / swing
    calculate contact forces with MPC
    calculate joint torques